## Slide 1: 21CSS201T COMPUTER ORGANIZATION AND ARCHITECTURE UNIT-1 Topic : Memory Locations and Addresses

## Slide 2: MEMORY HIERARCHY
Memory Hierarchy is to obtain the highest possible
access speed while minimizing the total cost of the memory system

## Slide 3: Memory Locations and Addresses
Memory consists of many millions of storage cells, each of which can store 1 bit.
Data is usually accessed in n-bit groups. n is called word length.
The memory of a computer can be schematically represented as a collection of words as shown in Figure 1.
second word
first word
Figure 1 Main Memory words.
n
bits
last word
i
th word
•
•
•
•
•
•

## Slide 4
MEMORY LOCATIONS AND ADDRESSES
Main memory is the second major subsystem in a computer. It consists of a collection of storage locations, each with a unique identifier, called an address.
Data is transferred to and from memory in groups of bits called words. A word can be a group of 8 bits, 16 bits, 32 bits or 64 bits (and growing).
If the word is 8 bits, it is referred to as a byte. The term “byte” is so common in computer science that sometimes a 16-bit word is referred to as a 2-byte word, or a 32-bit word is referred to as a 4-byte word.

## Slide 5
Main memory

## Slide 7
Address space
To access a word in memory requires an identifier. Although programmers use a name to identify a word (or a collection of words), at the hardware level each word is identified by an address.
The total number of uniquely identifiable locations in memory is called the address space.
For example, a memory with 64 kilobytes (16 address line required) and a word size of 1 byte has an address space that ranges from 0 to 65,535.

## Slide 8
Memory addresses are defined using unsigned binary integers.

## Slide 9
Example 1
A computer has 32 MB (megabytes) of memory. How many bits are needed to address any single byte in memory?
Solution
The memory address space is 32 MB, or 25 (25 × 20). This means that we need log2 225, or 25 bits, to address each byte.
Example 2
A computer has 128 MB of memory. Each word in this computer is eight bytes. How many bits are needed to address any single word in memory?
Solution
The memory address space is 128 MB, which means 27. However, each word is eight (23) bytes, which means that we have 224 words. This means that we need log2 224, or 24 bits, to address each word.

## Slide 10: MEMORY OPERATIONS
Today, general-purpose computers use a set of instructions called a program to process data.
A computer executes the program to create output data from input data
Both program instructions and data operands are stored in memory
Two basic operations requires in memory access
    Load operation (Read or Fetch)-Contents of specified memory location are read by processor
    Store operation (Write)- Data from the processor is stored in specified memory location

## Slide 11: Assignment of Byte Address
Big-endian and little-endian are terms that describe the order in which a sequence of bytes are stored in computer memory.
Big-endian is an order in which the "bigend" (most significant value in the sequence) is stored first (at the lowest storage address).
Little-endian is an order in which the “Little end" (least significant value in the sequence) is stored first (at the lowest storage address).

## Slide 13: Assignment of byte addresses
Little Endian (e.g., in DEC, Intel)
» low order byte stored at lowest address
» byte0 byte1 byte2 byte3
Eg: 46,78,96,54 (32 bit data)
H BYTE L BYTE
8000
8001
8002
8003
8004
54
96
78
46
¦

## Slide 14: Big Endian
Big Endian (e.g., in IBM, Motorolla, Sun, HP)
» high order byte stored at lowest address
» byte3 byte2 byte1 byte0
Programmers/protocols should be careful when transferring binary data between Big Endian and Little Endian machines

## Slide 15: Big-Endian and Little-Endian Assignments
2
k
4
-
2
k
3
-
2
k
2
-
2
k
1
-
2
k
4
-
2
k
4
-
0
1
2
3
4
5
6
7
0
0
4
2
k
1
-
2
k
2
-
2
k
3
-
2
k
4
-
3
2
1
0
7
6
5
4
Byte address
Byte address
(a) Big-endian assignment
(b) Little-endian assignment
4
W
ord
address
•
•
•
•
•
•
Byte and word addressing.
Big-Endian: lower byte addresses are used for the most significant bytes of the word
Little-Endian: opposite ordering. lower byte addresses are used for the less significant bytes of the word
Notes: 15

## Slide 16
In case of 16 bit data, aligned words begin at byte addresses of 0,2,4,………………………….
In case of 32 bit data, aligned words begin at byte address of 0,4,8,………………………….
In case of 64 bit data, aligned words begin at byte addresses of 0,8,16,………………………..
In some cases words can start at an arbitrary byte address also then, we say that word locations are unaligned